## Slide 1: Hak4Kidz 2019 Badge
Behind the scenes & Getting Started

## Slide 2: Here’s the Badge

## Slide 3: Here ARE the Badges Being Made

## Slide 4: ESP32 Main Processor Uses
Manufactured by Espressif Systems
ESP32-WROOM-32 MCU (Microcontroller Unit) Features
  Low-power sensor networks
  Voice encoding
  Music streaming
  MP3 decoding
  Video gaming
  Cool badges!
  Up to you!!!

## Slide 5: Meet ESP32

## Slide 6: ESP32 Specifications
Processors:
  CPU: Xtensa dual-core 32-bit LX6 microprocessor
    operating at 160 or 240 MHz and performing at up to 600 DMIPS
  Ultra low power (ULP) co-processor
Memory: 520 KiB SRAM
Wireless connectivity:
  Wi-Fi: 802.11 b/g/n
  Bluetooth: v4.2 BR/EDR and BLE
Source: Wikipedia https://en.wikipedia.org/wiki/ESP32

## Slide 7: ESP32 Specifications Continued
Peripheral interfaces:
  12-bit SAR ADC up to 18 channels
  2 × 8-bit DACs
  10 × touch sensors (capacitive sensing GPIOs)
  4 × SPI
  2 × I²S interfaces
  2 × I²C interfaces
  3 × UART
  SD/SDIO/CE-ATA/MMC/eMMC host controller
Source: Wikipedia https://en.wikipedia.org/wiki/ESP32
  SDIO/SPI slave controller
  Ethernet MAC interface with dedicated DMA and IEEE 1588 Precision Time Protocol support
  CAN bus 2.0
  Infrared remote controller (TX/RX, up to 8 channels)
  Motor PWM
  LED PWM (up to 16 channels)
  Hall effect sensor
  Ultra low power analog pre-amplifier

## Slide 8: ESP32 Specifications Continued
Security:
  IEEE 802.11 standard security features all supported,
  including WFA, WPA/WPA2 and WAPI
  Secure boot
  Flash encryption
  1024-bit OTP, up to 768-bit for customers
  Cryptographic hardware acceleration: AES, SHA-2, RSA, elliptic curve cryptography (ECC), random number generator (RNG)
Power management:
  Internal low-dropout regulator
  Individual power domain for RTC
  5μA deep sleep current
  Wake up from GPIO interrupt, timer, ADC measurements, capacitive touch sensor interrupt
Source: Wikipedia https://en.wikipedia.org/wiki/ESP32

## Slide 9: What else do the badges do?

## Slide 10: How to program the badge terms
Sketch - the name of an Arduino program.
Board – programmable hardware to install your sketch onto.
Code – the sketch instructions for the board to run.
IDE – Integrated Development Environment to create / edit your sketch.
Library – a way to extend your sketch by adding extra functionality.
Compile – converts human readable code to computer readable byte code.
Upload – compile and install your sketch to your board.
Verify – Arduino IDE feature to check your sketch code before you upload to the board

## Slide 11: How to program Using Arduino
Download & install the Arduino IDE from https://www.arduino.cc/en/Main/Software for your computer type.
Open Preferences
Go to Additional Boards Manager URLs:
Enter https://dl.espressif.com/dl/package_esp32_index.json

## Slide 12: How to program – Add the ESP32 Board Manager
Tools / Board / Board Manager search for ‘ESP32’.
Click Install. Wait.
Go to https://github.com/Hak4Kidz/H4K-badge-2019
Download libraries from software / Arduino / libraries
Put files in Docs / Arduino / libraries folder

## Slide 13: How to program – Connect Badge Hardware
Remove the badge from your neck
Connect USB cable end to computer
Connect micro-USB cable end to badge connector
Arduino / Tools / Board “ESP32 Wrover Module”
Select Tools / Port and the port name ie COM 3
Test connection using Tools / Get Board Info

## Slide 14: How to program – Open the badge sketch
Download badge sketch from github
  https://github.com/Hak4Kidz/H4K-badge-2019
File named 2019_Tyro_Badge.ino
Arduino IDE / File / Open / 2019_Tyro_Badge.ino
Ctrl + F to find ‘myName’
  Check if case sensitivity is enabled
Arrow down to “My name is Tinker!”
Change “Tinker” to your name or handle.
Click “Upload” icon

## Slide 15: What was not covered Today
Hardware addressing
LEDs monochrome and RGB
LED Driver
LCD graphics library features
ESP32 advanced features
SOA connectors
HACK connectors

## Slide 16: What’s Next?
Creativity
Practice
Master

## Slide 17: Enjoy!
Healwhans@hak4kidz.com
@Hak4Kidz
@Dschwartzberg
Facebook